## Slide 2: Commonalities to Fast and efficient Fourier transform hardware implementations
Separating transform to be across rows and columns
Butterfly networks
FFT in place
Decimation in Frequency
Factorization to reduce complex operations within FFT from 4 multiplications and 2 additions to 3 multiplications and 3 additions
CORDIC
conjugate symmetry so ~ half the butterfly size

## Slide 3: Design Tradeoffs
 | Memory efficiency | Computational latency | Utilization
Delay Feedback radix-2 | X |  | X
Delay Feedback radix-4 | X | X | 
Delay commute radix-2 |  |  | X
Delay commute radix-4 |  | X | 

## Slide 4: Design tricks
If total reconfig time will be of issue, we can make a larger FFT engines out of smaller engines to support wide range of transforms
  May also help to reduce power
  Tradeoff is shared FFT engine as opposed to dedicated engines per layer