## Slide 1: CNN Accelerator Implementation Plan

## Slide 2: CNN Acceleration

## Slide 3: System Architecture

## Slide 4: CNN Layer Attributes
Kernel-Width {Wide, Narrow}
  Describes the relative width ‘KW’ of a single kernel
  Also corresponds to input map width
  Narrow: ‘KW’ =< 8
  Wide: ‘KW’ > 8
Layer-Width {Wide, Narrow}
  Describes the relative width ‘LW’ of a layer
  Narrow: ‘LW’ =< 8
  Wide: ‘LW’ > 8

## Slide 5: CNN Layer Attributes (cont.)
Pooling
  Specifies whether the layer includes a pooling stage
  Pooling subsamples a 2D window from a convolved input map
  The subsampling operation can be min, max, average, etc.
  The stride of the subsampling window determines the dimension of pooling output map
  Example: the result of convolving a 256x256x3 input with a 3x3x3 kernel is a 256x256x1 map (ignoring boundary effects). Passing this map to a MAX pooling operator with 2x2 stride results in a 128x128x1 map. Each pixel in this map corresponds to the max value in the convolved map at window centered at the pixel

## Slide 6: CNN Layer Attributes (cont.)
Activation
  Specifies whether the layer includes an activation stage
  Activation transforms each input map pixel according to f(x)
  Activation does not alter the dimensions of the input map
  The implementation of Activation is relatively cheap when f(x) =
    Rectified Linear (ReLU)
  Activation may require LUT based interpolation when f(x) =
    Sigmoid
    Hyperbolic tangent
    Other differentiable functions of ‘x’

## Slide 7: CNN Layer Attributes (cont.)
Squeeze
  Specifies whether the layer implements a map reducing “Squeeze” operation
  Squeezing a layer reduces the width of the output map leaving the layer
    The width of an output map is equal to the number of kernels in the layer
    By performing a convolution across the original K output maps, a single final output map is produced
    Note that there may be several (SQ) Squeeze kernels, each producing a single output map
    Generally |SQ| << K
    Typically the squeeze kernel is a 1x1 but is not necessary
Stretch (Expand)
  Specifies whether the layer implements a map increasing “Stretch” operation
  Stretching a layer increases the width of the output map leaving the layer
    Operation is identical to “Squeeze” however the number of Stretch (ST) kernels follows: |ST| > K
    Typically the stretch kernel is a 1x1 but is not necessary

## Slide 8: Accelerating a Single Kernel

## Slide 9: Single Convolution Engine
Single Engine capable of performing:
  3x3x1 convolution (CPI = 0.9)
  1x1x10 convolution (CPI = 1.0)
Uses optimized DSP48E2 tile architecture consisting of two DSP48E2 macros
Operates at 5x datapath clock- (500Mhz)
Requires pixels to be evenly distributed across row-buffer banks
A single row buffer bank consists of two row buffers of max length = L. A row buffer bank has a dedicated connection to an adjacent DSP48E2 unit in the enclosing DSP48E2 tile
DSP48E2 Tile

## Slide 10: Adaptive Window Engine (AWE)
Dual convolution engines capable of performing the following:
  3x3x2 (CPI = 0.9)
  5x5x1 (CPI = 1.25)
  1x1x20 (CPI = 1.0)
Support 3x3 or 5x5 pooling
Requires pixels to be evenly distributed across row-buffer banks
In pooling mode the row-buffers feed a MAX/MIN/AVG module. Pooling can be performed over the two row buffers of a single engine or over the four combined row-buffers of two engines.

## Slide 11: Load Balancing in AWE
To minimize logic delay, each buffer is directly connected to the adjacent DSP48 in the tile.
Since we are overclocking to reduce resource utilization of DSP48, it is important that each DSP48 as nearly equal work
  Row renaming is accomplished by (1) reordering of weights based on the current row we operating on, and (2) a specific matriculation of rows across the buffers
  In the case of odd kernels, a duplicate of one row is required in the buffer
Dual
Row Buffers
Dual
Row Buffers
Row Matriculation for 3x3 Config
BRAM0
BRAM1
BRAM2
BRAM3

## Slide 12: Load Balancing in AWE
Row Matriculation for 5x5 Config

## Slide 14: Row Buffer Logic
Supports up to 512 x 512 images
BRAMS are 1024 elements deep
Each Convolution Engines use 2 dual ported (one port for reading, another port to write while reading for row matriculation) 1024 element BRAM’s as row buffers; Each BRAM is partitioned into 512 chunks, to support up to 4 rows
  Switching to different partitions on different row combinations is accomplished by toggling MSB, gray code counter, and OR’ing the LSB with a parity bit
Convolution engines start 1 cycle after each other

## Slide 15
X
X
1023
512
511
0
Image
0 1 2 N
Cycle 0
0 | . | . | . | . | . | . | . | . | . | . | . | . | 0 | 0
0 | . | . | . | . | . | . | . | . | . | . | . | . | 0 | 1
MSB
0
1
0 2 512 513 514
MSB
LSB
OR
Row 1
Row 0
Row 1
Row 0
0 1 2 N
BRAM0
BRAM1
BRAM0
Addr Bits
BRAM1
Addr Bits
Preloaded Sequence
LSB

## Slide 16
Image
0 1 2 N
X
X
Cycle 1
Row 2
Row 0
0 | . | . | . | . | . | . | . | . | . | . | . | . | 0 | 0
0 | . | . | . | . | . | . | . | . | . | . | . | . | X | X
2
X
0 2 512 513 514
Weight Value of 0 Needed here
1023
512
511
0
Row 2
Row 1
Row 0
Row 1
Row 0
0 1 2 N
BRAM0
BRAM1
BRAM0
Addr Bits
BRAM1
Addr Bits
Preloaded Sequence
MSB
MSB
LSB
LSB

## Slide 17
X
X
1023
512
511
0
Image
0 1 2 N
Cycle 2
Row 2
Row 1
Row 0
1 | . | . | . | . | . | . | . | . | . | . | . | . | 0 | 0
1 | . | . | . | . | . | . | . | . | . | . | . | . | 0 | 0
512
512
0 2 512 513 514
Row 1
Row 0
0 1 2 N
BRAM0
BRAM1
BRAM0
Addr Bits
BRAM1
Addr Bits
Preloaded Sequence
MSB
MSB
LSB
LSB

## Slide 18
X
X
Image
0 1 2 N
0 1 2 N
Cycle 3
1 | . | . | . | . | . | . | . | . | . | . | . | . | 0 | 0
1 | . | . | . | . | . | . | . | . | . | . | . | . | 0 | 0
513
513
0 2 512 513 514
1023
512
511
0
Row 2
Row 1
Row 0
Row 1
Row 0
BRAM0
BRAM1
BRAM0
Addr Bits
BRAM1
Addr Bits
Preloaded Sequence
MSB
MSB
LSB
LSB

## Slide 19
X
X
Image
0 1 2 N
Cycle 4
Row 0
1 | . | . | . | . | . | . | . | . | . | . | . | . | 0 | 0
1 | . | . | . | . | . | . | . | . | . | . | . | . | 0 | 0
514
514
0 2 512 513 514
1023
512
511
0
Row 2
Row 1
Row 0
Row 1
Row 0
0 1 2 N
BRAM0
BRAM1
BRAM0
Addr Bits
BRAM1
Addr Bits
Preloaded Sequence
MSB
MSB
LSB
LSB

## Slide 20: Weight Table logic
1 dual ported weight table per convolution engine
  Weights are supplied from both ports

## Slide 21: Weight Table logic (3x3)
0 1 2
0 1 2
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9

## Slide 22: Adaptive Window Quad
Four cascaded Adaptive Window Engines (AWE)
Quad shares a single bidirectional Tile Router port
Supports Narrow Convolution or wide Pooling
Routable output for the following:
  3x3x8, 5x5x4, or 1x1x80 convolutions plus optional activation and pooling
  8-3x3 pooling or 4-5x5 pooling

## Slide 23: Accelerating Wide Kernels
Adaptive Window Quads can be cascaded at the output/input of the top/bottom quads respectively
Quads are asynchronous wrt. each other requiring shallow buffering at the interface
AW Quad Cascade Path

## Slide 24: Accelerating Multiple Kernels (Wide Layers)

## Slide 25: Accelerating multiple Kernels
Make full use of current row buffer contents across all kernels
  Since kernels share identical input maps (different kernel weights)
  Reduces demand on Input interface particularly for Wide Layers

## Slide 26: Fetch-Aggregate-Store (FAS) Unit
The FAS unit is responsible for:
  fetching data and forwarding to one or more AWP
  Accumulating the partial maps arriving from multiple AWPs and/or memory
  Storing maps to memory in particular format
Each FAS has two dedicated SOC-IT interfaces for I/O
  It is possible for FAS to share its I/O bandwidth with other FAS in a “teaming” configuration (advanced)
From the software perspective, a FAS represents a CNN accelerator
  Application software acquires a resource lock on a FAS for the duration of a CNN compute
  Software invokes the FAS which in turn dispatches work to AWP at a per layer granularity

## Slide 27: Fetch-Aggregate-Store (FAS) Unit

## Slide 28
Single Adaptive Window Processor
Kintex Ultrascale

## Slide 29: Implementation Roles
AWP – Ikenna & Geetha
FAS – Saambhavi
Functional Verification – Kevin & Ikenna
Software development – Kevin

## Slide 30
Map size: Depth x NumRows x NumCols
  8x20x20
Kernel size: NumKernels x Depth x NumKrnlRows x NumKrnlCols
  5x8x3x3
Stride is 1
No padding
No UpSampling

## Slide 31
Image Input Format
    [D0C0R0, D1C0R0, ... D7C0R0] [D0C1R0, D1C1R0, ... D7C1R0] ....... [D0C19R0, D1C19R0, ... D7C19R0]
    [D0C0R1, D1C0R1, ... D7C0R0] [D0C1R0, D1C1R1, ... D7C1R0] ....... [D0C19R1, D1C19R1, ... D7C19R1]
    .
    .
    .
    .
    [D0C0R19, D1C0R19, ... D7C0R19] [D0C1R19, D1C1R19, ... D7C1R19] ....... [D0C19R19, D1C19R18, ... D7C19R19]

## Slide 32
D0C0R0
D1C0R0
D2C0R0
D3C0R0
D4C0R0
D5C0R0
D6C0R0
D7C0R0
AWE ROW BUFFER0
AWE ROW BUFFER1
AWE ROW BUFFER2
AWE ROW BUFFER3
AWE ROW BUFFER4
AWE ROW BUFFER5
AWE ROW BUFFER6
AWE ROW BUFFER7

## Slide 33
D0C1R0
D1C1R0
D2C1R0
D3C1R0
D4C1R0
D5C1R0
D6C1R0
D7C1R0
AWE ROW BUFFER0
AWE ROW BUFFER1
AWE ROW BUFFER2
AWE ROW BUFFER3
AWE ROW BUFFER4
AWE ROW BUFFER5
AWE ROW BUFFER6
AWE ROW BUFFER7

## Slide 34
D0C19R0
D1C19R0
D2C19R0
D3C19R0
D4C19R0
D5C19R0
D6C19R0
D7C19R0
AWE ROW BUFFER0
AWE ROW BUFFER1
AWE ROW BUFFER2
AWE ROW BUFFER3
AWE ROW BUFFER4
AWE ROW BUFFER5
AWE ROW BUFFER6
AWE ROW BUFFER7

## Slide 35
D0C0R1
D1C0R1
D2C0R1
D3C0R1
D4C0R1
D5C0R1
D6C0R1
D7C0R1
AWE ROW BUFFER0
AWE ROW BUFFER1
AWE ROW BUFFER2
AWE ROW BUFFER3
AWE ROW BUFFER4
AWE ROW BUFFER5
AWE ROW BUFFER6
AWE ROW BUFFER7

## Slide 36
D0C1R1
D1C1R1
D2C1R1
D3C1R1
D4C1R1
D5C1R1
D6C1R1
D7C1R1
AWE ROW BUFFER0
AWE ROW BUFFER1
AWE ROW BUFFER2
AWE ROW BUFFER3
AWE ROW BUFFER4
AWE ROW BUFFER5
AWE ROW BUFFER6
AWE ROW BUFFER7

## Slide 37
D0C19R1
D1C19R1
D2C19R1
D3C19R1
D4C19R1
D5C19R1
D6C19R1
D7C19R1
AWE ROW BUFFER0
AWE ROW BUFFER1
AWE ROW BUFFER2
AWE ROW BUFFER3
AWE ROW BUFFER4
AWE ROW BUFFER5
AWE ROW BUFFER6
AWE ROW BUFFER7

## Slide 38
D0C0R19
D1C0R19
D2C0R19
D3C0R19
D4C0R19
D5C0R19
D6C0R19
D7C0R19
AWE ROW BUFFER0
AWE ROW BUFFER1
AWE ROW BUFFER2
AWE ROW BUFFER3
AWE ROW BUFFER4
AWE ROW BUFFER5
AWE ROW BUFFER6
AWE ROW BUFFER7

## Slide 39
D0C1R19
D1C1R19
D2C1R19
D3C1R19
D4C1R19
D5C1R19
D6C1R19
D7C1R19
AWE ROW BUFFER0
AWE ROW BUFFER1
AWE ROW BUFFER2
AWE ROW BUFFER3
AWE ROW BUFFER4
AWE ROW BUFFER5
AWE ROW BUFFER6
AWE ROW BUFFER7

## Slide 40
D0C19R19
D1C19R19
D2C19R19
D3C19R19
D4C19R19
D5C19R19
D6C19R19
D7C19R19
AWE ROW BUFFER0
AWE ROW BUFFER1
AWE ROW BUFFER2
AWE ROW BUFFER3
AWE ROW BUFFER4
AWE ROW BUFFER5
AWE ROW BUFFER6
AWE ROW BUFFER7

## Slide 41
3x3 Kernel Input Format

## Slide 42
Ideally output will be 5x18x18
  However output is be 5x18x20, with the result in the top left
    [R0C0D0, R0C1D0, ... R0C19D0] [R0C0D1, R0C1D1, ... R0C19D1] ….... [R0C19D4, R0C1D4, ... R0C19D4]
    [R1C0D0, R1C1D0, ... R1C19D0] [R1C0D1, R1C1D1, ... R1C19D1] ….... [R1C19D4, R1C1D4, ... R1C19D4]
    .
    .
    .
    [R17C0D0, R17C1D0, ... R17C19D0] [R17C0D1, R17C1D1, ... R17C19D1] ….... [R17C0D4, R17C1D4, ... R17C19D4]

## Slide 43
For 3x3 followed by 1x1 Ideally output will be 5x18x18
  [C0R0D0, C0R0D1, ... C0R0D4] [C1R0D0, C1R0D1, ... C1R0D4] ............ [C19R0D0, C19R0D1, ... C19R0D4]
  [C0R1D0, C0R1D1, ... C0R1D4] [C1R1D0, C1R1D1, ... C1R1D4] ............ [C19R1D0, C19R1D1, ... C19R1D4]
  .
  .
  .
  [C0R17D0, C0R17D1, ... C0R17D4] [C1R17D0, C1R17D1, ... C1R17D4] ............ [C19R17D0, C19R17D1, ... C19R17D4]