## Slide 1: CNN Accelerator Implementation Plan

## Slide 2: CNN Acceleration

## Slide 3: System Architecture

## Slide 4: CNN Layer Attributes
Kernel-Width {Wide, Narrow}
  Describes the relative width ‘KW’ of a single kernel
  Also corresponds to input map width
  Narrow: ‘KW’ =< 8
  Wide: ‘KW’ > 8
Layer-Width {Wide, Narrow}
  Describes the relative width ‘LW’ of a layer
  Narrow: ‘LW’ =< 8
  Wide: ‘LW’ > 8

## Slide 5: CNN Layer Attributes (cont.)
Pooling
  Specifies whether the layer includes a pooling stage
  Pooling subsamples a 2D window from a convolved input map
  The subsampling operation can be min, max, average, etc.
  The stride of the subsampling window determines the dimension of pooling output map
  Example: the result of convolving a 256x256x3 input with a 3x3x3 kernel is a 256x256x1 map (ignoring boundary effects). Passing this map to a MAX pooling operator with 2x2 stride results in a 128x128x1 map. Each pixel in this map corresponds to the max value in the convolved map at window centered at the pixel

## Slide 6: CNN Layer Attributes (cont.)
Activation
  Specifies whether the layer includes an activation stage
  Activation transforms each input map pixel according to f(x)
  Activation does not alter the dimensions of the input map
  The implementation of Activation is relatively cheap when f(x) =
    Rectified Linear (ReLU)
  Activation may require LUT based interpolation when f(x) =
    Sigmoid
    Hyperbolic tangent
    Other differentiable functions of ‘x’

## Slide 7: CNN Layer Attributes (cont.)
Squeeze
  Specifies whether the layer implements a map reducing “Squeeze” operation
  Squeezing a layer reduces the width of the output map leaving the layer
    The width of an output map is equal to the number of kernels in the layer
    By performing a convolution across the original K output maps, a single final output map is produced
    Note that there may be several (SQ) Squeeze kernels, each producing a single output map
    Generally |SQ| << K
    Typically the squeeze kernel is a 1x1 but is not necessary
Stretch (Expand)
  Specifies whether the layer implements a map increasing “Stretch” operation
  Stretching a layer increases the width of the output map leaving the layer
    Operation is identical to “Squeeze” however the number of Stretch (ST) kernels follows: |ST| > K
    Typically the stretch kernel is a 1x1 but is not necessary

## Slide 8: Accelerating a Single Kernel

## Slide 9: Single Convolution Engine
Single Engine capable of performing:
  3x3x1 convolution (CPI = 0.9)
  1x1x10 convolution (CPI = 1.0)
Uses optimized DSP48E2 tile architecture consisting of two DSP48E2 macros
Operates at 5x datapath clock- (500Mhz)
Requires pixels to be evenly distributed across row-buffer banks
A single row buffer bank consists of two row buffers of max length = L. A row buffer bank has a dedicated connection to an adjacent DSP48E2 unit in the enclosing DSP48E2 tile
DSP48E2 Tile

## Slide 10: Adaptive Window Engine (AWE)
Dual convolution engines capable of performing the following:
  3x3x2 (CPI = 0.9)
  5x5x1 (CPI = 1.25)
  1x1x20 (CPI = 1.0)
Support 3x3 or 5x5 pooling
Requires pixels to be evenly distributed across row-buffer banks
In pooling mode the row-buffers feed a MAX/MIN/AVG module. Pooling can be performed over the two row buffers of a single engine or over the four combined row-buffers of two engines.

## Slide 11: Load Balancing in AWE
To minimize logic delay, each buffer is directly connected to the adjacent DSP48 in the tile.
Since we are overclocking to reduce resource utilization of DSP48, it is important that each DSP48 as nearly equal work
  Row renaming is accomplished by (1) reordering of weights based on the current row we operating on, and (2) a specific matriculation of rows across the buffers
  In the case of odd kernels, a duplicate of one row is required in the buffer
Dual
Row Buffers
Dual
Row Buffers
Row Matriculation for 3x3 Config

## Slide 12: Load Balancing in AWE
Row Matriculation for 5x5 Config

## Slide 13: Adaptive Window Quad
Four cascaded Adaptive Window Engines (AWE)
Quad shares a single bidirectional Tile Router port
Supports Narrow Convolution or wide Pooling
Routable output for the following:
  3x3x8, 5x5x4, or 1x1x80 convolutions plus optional activation and pooling
  8-3x3 pooling or 4-5x5 pooling

## Slide 14: Accelerating Wide Kernels
Adaptive Window Quads can be cascaded at the output/input of the top/bottom quads respectively
Quads are asynchronous wrt. each other requiring shallow buffering at the interface
AW Quad Cascade Path

## Slide 15: Accelerating Multiple Kernels (Wide Layers)

## Slide 16: Accelerating multiple Kernels
Make full use of current row buffer contents across all kernels
  Since kernels share identical input maps (different kernel weights)
  Reduces demand on Input interface particularly for Wide Layers

## Slide 17: Fetch-Aggregate-Store (FAS) Unit
The FAS unit is responsible for:
  fetching data and forwarding to one or more AWP
  Accumulating the partial maps arriving from multiple AWPs and/or memory
  Storing maps to memory in particular format
Each FAS has two dedicated SOC-IT interfaces for I/O
  It is possible for FAS to share its I/O bandwidth with other FAS in a “teaming” configuration (advanced)
From the software perspective, a FAS represents a CNN accelerator
  Application software acquires a resource lock on a FAS for the duration of a CNN compute
  Software invokes the FAS which in turn dispatches work to AWP at a per layer granularity

## Slide 18: Fetch-Aggregate-Store (FAS) Unit

## Slide 19
Single Adaptive Window Processor
Kintex Ultrascale

## Slide 20: Implementation Roles
AWP – Ikenna & Geetha
FAS – Saambhavi
Functional Verification – Kevin & Ikenna
Software development – Kevin